## Slide 1: TOUCH SENSING MODULE (TSI)

## Slide 2: Goals
Understanding the Capacitive Touch Sensor
Understanding the Touch Sensing Interface (TSI) module in KL25Z
Implementing basic drivers for TSI module

## Slide 3: INTRODUCTION
Touch Sensing Technology Types:
1. Resistive
2. Capacitive
Capacitive Touch Types:
1. Self- Capacitance
2. Mutual Capacitance

## Slide 4: BASICS
Mutual Capacitance Configuration:
Two electrodes: Transmitter and Receiver
Capacitance formed between electrodes
and the dielectric between them.
Microcontroller sends electric pulses
to generate electromagnetic field between
the electrodes.
Human finger decreases the
electromagnetic field when in touch with
the electrode.

## Slide 5: BASICS
Self Capacitance Configuration:
Only one electrode is used.
Capacitance is formed between electrode
and ground plane.
Internal circuit drives the electrode
and senses the charge and discharging time
to measure the capacitance.
Change in electromagnetic field when
finger is in close contact with electrode
which will change the charge and discharge time, thereby changing the capacitance measured.

## Slide 6: KL25Z CIRCUIT LAYOUT

## Slide 7: TSI MODULE FEATURES:
Support up to 16 external electrodes
Configurable software or hardware scan trigger
Capability to wake MCU from low power modes
Support DMA data transfer
There are two ways of programming the TSI module:
Using the TSS library.
Writing your own embedded drivers

## Slide 8: TSI MODULE REGISTERS
General Control and Status Register (TSI0_GENCS)
Threshold register (TSI0_TSHD)
DATA register (TSI0_DATA)

## Slide 9: General Control and Status Register (TSI0_GENCS)
OUTRGF Out of range flag.
Set if result is out of range from the values in the Threshold register (TSHD).
ESOR End-of-scan or out-of-range interrupt selection.
0 = Interrupt on out-of-range
1 = Interrupt on end-of-scan

## Slide 10: CONTINUED…
MODE Analog mode set up and status bits.
Four modes available.
Mode 0: non-noise mode.
Mode 1 and 2: Noise Threshold detection mode
Mode 3: Automatic Nosie detection mode
REFCHRG Reference oscillator charge/discharge value.
Eight values from 500 nA to 64uA available.
DVOLT Select oscillator voltage rails.
Four levels available.

## Slide 11: CONTINUED…
EXTCHRG Electrode oscillator charge/discharge value.
Eight values from 500 nA to 64uA available.
PS Prescaler value.
Frequency divisor for clock can be from 1 to 128.
NSCN Electrode oscillator count used in making a scan.
Value can be from 1 to 32.
TSIEN TSI module enable.
0 = Module disabled
1 = Module enabled

## Slide 12: CONTINUED…
TSIIEN TSI module interrupt enable.
0 = Interrupt disabled
1 = Interrupt enabled
STPE TSI STOP Enable.
Enables TSI module to operate in low-power modes.
0 = TSI disabled in low-power mode
1 = TSI runs in all low-power modes
STM Scan trigger mode.
0 = Software triggers scan
1 = Hardware clock triggers scan

## Slide 13: CONTINUED…
SCNIP Scan in progress status.
0 = No scan in progress
1 = Scan in progress
EOSF End of scan flag.
0 = Scan incomplete
1 = Scan complete
Write 1 to clear this flag.
CURSW Current sources for oscillators swapped.
0 = Current source pair not swapped
1 = Current source pair swapped

## Slide 14: CONTINUED…
SCNIP Scan in progress status.
0 = No scan in progress
1 = Scan in progress
EOSF End of scan flag.
0 = Scan incomplete
1 = Scan complete
Write 1 to clear this flag.
CURSW Current sources for oscillators swapped.
0 = Current source pair not swapped
1 = Current source pair swapped

## Slide 15: Threshold register (TSI0_TSHD)
THRESH TSI wakeup channel high threshold value.
THRESL TSI wakeup channel low threshold value.
DATA register (TSI0_DATA)

## Slide 16: CONTINUED…
TSICH TSI channel select.
These bits select the channel to be sampled. The TSI supports a maximum of sixteen channels.
DMAEN DMA transfer enabled.
This bit determines whether the module generates a DMA request.
SWTS Software trigger start.
When this bit is set, the TSI starts a scan.
0 = No effect.
1 = Start a scan on the channel specified.
TSICNT TSI conversion counter value.
It is a measure of the electrode capacitance.

## Slide 17: Code Implementation
Implemented in both Busy- Wait and Interrupt
Selectable using Macro
Kindly refer the Code for further explanation